A signal generator
Based on an ATMEGA8
By Michael Tempest, December 2015

Use timer 1 – 16-bit timer.
Timer 1 has a prescaler: system clock divided by 1, 8, 64, 256, 1024
Phase 1: square wave output on OC1A
Phase 2: PWM output on OC1B

Interface is N5110 LCD with pushbuttons
The library I have does not need an SPI peripheral.
The LCD is a 3.3V device. Level-translation will be required.
Pushbuttons to ground with internal pull-up resistors

Use the internal RC oscillator. Internal oscillator is calibrated to within 3%.
Store a correction figure in EEPROM.

Use UART for debug-message port.
In System Programming requires SCK, MISO, MOSI and RESET.

ISP	1 – PC6 (RESET)	Pinout	(SCL) PC5 – 28
Debug port	2 – PD0 (RXD)		(SDA) PC4 – 27
Debug port	3 – PD1 (TXD)		(ADC3) PC3 – 26
PB (up)	4 – PD2 (INT0)		(ADC2) PC2 – 25
PB (down)	5 – PD3 (INT1)		(ADC1) PC1 – 24
PB (next)	6 – PD4 (T0)		(ADC0) PC0 – 23
VCC	7 – VCC		GND – 22	GND
GND	8 – GND		AREF – 21	NC
PB	9 – PB6		AVCC – 20	VCC
LCD	10 – PB7		(SCK) PB5 – 19	ISP
CS (LCD)	11 – PD5 (T1)		(MISO) PB4 – 18	ISP
RST (LCD)	12 – PD6 (AIN0)		(MOSI) PB3 – 17	ISP
DC (LCD)	13 – PD7 (AIN1)		(OC1B) PB2 – 16	Output
Backlight	14 – PB0 (ICP1)		(OC1A) PB1 – 15	Output

# Functions
Set frequency
Display frequency
Fine calibration
OSCCAL calibration
Enable / disable output
Save settings to EEPROM automatically
Adjust blacklight

# User interface design
LCD w x h is 84 x 48.
Small font is 6x8 characters, giving 6 rows of 14 characters
Medium numbers font is 12x16, giving 3 rows of 7 characters
Large numbers font is 14x24, giving 2 rows of 6 characters

Layout:
1			2			3			.			4			5
W	a	v		e	F		o	r	m				U	n		i	t
								O	f	f
		P		a	r		a	m	:	V	a		l	u		e

The 7-segment numbers are ugly. These numbers from GIMP's Monospace Bold are used instead:

4 buttons, two to each side
Left top: increment value, long push to auto-increment
Left bottom: decrement value, long push to auto-increment
Right top: toggle on/off, long push
Right bottom: select next parameter, long push selects frequency

Parameters: frequency, period, scale, waveform, duty-cycle, amplitude, contrast, fine calibrate, OSCCAL

Numbers at y=0, three text rows at y=24,32,40

# Details
## Power
The LCD wants between 2.7V and 3.3V. An LM317 with 330Ω and 470Ω produces about 3V.
## Voltage translation
10kΩ resistors will provide adequate voltage translation.
## Clocking
The system is driven at 8 MHz by the internal oscillator.
CKSEL3..0 is 0100
CKOPT must be 1
SUT1..0 should be 10 (for slowly rising power)
## SPI-like inteface to LCD controller
Maximum LCD clock frequency is 4MHz.
Instructions must be sent MSB first. LCD controller samples SDIN on the rising edge of SCLK.
Based on the LCD5110_Graph driver, the clock should be high when idle.
SPCR: SPE must be 1 to enable SPI. DORD must be 0 to send MSB first. MSTR must be 1 for master. CPOL must be 1 for high when idle. CPHA must be 1 to sample data on the trailing i.e. rising edge. SPR1 and SPR0 must be 0 for fosc/2 or fosc/4 (depends on SPI2X).
SPI2X can be left at 0. 2MHz clock should be fast enough. (On the breadboard, I had to clock it at fosc/128 i.e. 62.5kHz)
## Input monitoring
Discretes should be sampled, and keypresses detected, in an interrupt routine to prevent missing keypresses.
Timer 2 will be used in CTC mode for this. It will tick approximately every 20ms.
Timer 2's prescaler must be set for divide-by-1024.
## Fuses
Atmega8 has 2 fuse bytes.
High fuse byte
Bit	Name	Description	State	Hex
7	RSTDISBL	Select if PC6 is I/O pin (0) or RESET pin (1)	1	80
6	WDTON	WDT always on (0) or controlled by WDTCR (1)	1	40
5	SPIEN	Enable Serial Program and Data Downloading (0) or disable (1)	0	00
4	CKOPT	Oscillator options	1	10
3	EESAVE	EEPROM memory is preserved through the Chip Erase (0) or not preserved i.e. erased (1)	0	00
2	BOOTSZ1		0	00
1	BOOTSZ0		0	00
0	BOOTRST	Select Reset Vector	1	01
				D1

Low fuse byte
Bit	Name	Description	State	Hex
7	BODLEVEL	Brown-out detector trigger level	1	80
6	BODEN	Brown-out detector enable (0) or disable (1)	1	40
5	SUT1	Select start-up time	1	20
4	SUT0	Select start-up time	0	00
3	CKSEL3	Select clock source	0	00
2	CKSEL2	Select clock source	1	04
1	CKSEL1	Select clock source	0	00
0	CKSEL0	Select clock source	0	00
				E4