A signal generator

Based on an ATMEGA8.

Use timer 1 – 16-bit timer.
Timer 1 has a prescaler: system clock divided by 1, 8, 64, 256, 1024
Phase 1: square wave output on OC1A
Phase 2: PWM output on OC1B

Interface is N5110 LCD with pushbuttons
The library I have does not need an SPI peripheral.
The LCD is a 3.3V device. Level-translation will be required.
Pushbuttons to ground with internal pull-up resistors

Use the internal RC oscillator. Internal oscillator is calibrated to within 3%.
Store a correction figure in EEPROM.

Use UART for debug-message port.
In System Programming requires SCK, MISO, MOSI and RESET.

	1 – PC6 (RESET)	Pinout	(SCL) PC5 – 28
Debug port	2 – PD0 (RXD)		(SDA) PC4 – 27
Debug port	3 – PD1 (TXD)		(ADC3) PC3 – 26
	4 – PD2 (INT0)		(ADC2) PC2 – 25
	5 – PD3 (INT1)		(ADC1) PC1 – 24
	6 – PD6 (T0)		(ADC0) PC0 – 23
VCC	7 – VCC		GND – 22	GND
GND	8 – GND		AREF – 21	NC
	9 – PB6		AVCC – 20	VCC
	10 – PB7		(SCK) PB5 – 19	ISP
	11 – PD5 (T1)		(MISO) PB4 – 18	ISP
	12 – PD6 (AIN0)		(MOSI) PB3 – 17	ISP
	13 – PD7 (AIN1)		(OC1B) PB2 – 16	Output
	14 – PB0 (ICP1)		(OC1A) PB1 – 15	Output

Functions

Set frequency
Display frequency
Calibrate
Enable / disable output
Save settings to EEPROM automatically

User interface design

LCD w x h is 84 x 48.
Small font is 6x8 characters, giving 6 rows of 14 characters
Medium numbers font is 12x16, giving 3 rows of 7 characters
Large numbers font is 14x24, giving 2 rows of 6 characters

1			2			3			.			4			5
W	a	v		e	F			O	f	f			U	n		i	t
		P		a	r		a	m	:	V	a		l	u		e
A	d	j								S	e		l	e		c	t

4 buttons, two to each side
Left top: increment value, long push to auto-increment
Left bottom: decrement value, long push to auto-increment
Right top: toggle on/off, long push
Right bottom: select next parameter, long push selects frequency

Parameters: frequency, scale, waveform, calibrate